###### Multifunctional Handheld Wireless Laser Scanner & Data Collector (Build in Laser, RFID Reader and Blue Tooth)

HDC-7630S      HDC-7630D        Cradle

Laser & BT, Class I, 100m      Long Range RFID design <= 20 cm

Features:

* Handheld bar code laser scanner & Data Collector.

* Laser reader (1D) or CMOS (1D/2D)

* OLED display, 128 x 64 resolution, two colors.

* Main body interfaces could be RS232/USB/Blue Tooth.

* Build in Blue Tooth, Class I, transmission distance <= 100 m.

* Build in RFID reader/writer, Mifare, I-Code, EPC….

* Rechargeable Li-ion battery 1200mA in main body or 2200mA in gun grid,

scanning time >= 10,000.

* 19 keys keypad for Alphanumeric input.

* Base Station for hand free scanning, data transmission and battery charging.

Specifications

| CPU | ARM7, 32 bit RISC, 60MHz |
| --- | --- |
| Memory | RAM: 16kB 512kB Flash ROM Extended Memory: 1MB Flash ROM |
| Display | OLED 128 x 64, two colors (Yellow/Green) |
| Keypad | 19 keys or 7 keys |
| Communication | RS232, 9600~115200 bps Ethernet (option) Blue Tooth Class I/II (option) RFID 13.56MHz (option) |
| Battery | Li-ion 1200mAH or 2200mAH |
| Power Adapter | DC6V, 1.5A, AC 100~240V, 50~60Hz |
| Dimension | 105mm (L) x 57mm (W) x 24 mm (H) |
| Weight | 80 g (no battery) |
| Power Consumption | Idle: 8mA, Operation: 100mA (includes Laser) |
| Scan Module | Laser |
| Full Charge Scanning | > 10,000 times |
| Input Modes | Keypad, Laser, RFID (option) |
| Bar Code Symbologies | UPC, EAN, Code 39, Code 128, Interleaved 2 of 5 |
| RFID readers | Mifare, I-Code |
| Operating Temperature | -0℃ to 40℃ |
| Relative Humidity | 5% to 95% (Non-condensing) |
| Drop | 1.2m |
| Rain and Dust Resistance | IP54 |
| Dimension/ Weight | 60 mm(W) x 56 mm(L) x 29.5(H) mm/ 33g (except cable) |
| Accessories | Rubber housing, Waist clip, Li-ion battery, Communication cable, Cradle |
| Handheld | RFID reader | RFID & Laser | Waist Clip |