Surface Acoustic Wave Touch Screen

Touch Panel and controller

This new type of Surface Acoustic Wave touchscreen used “DFR” & “Bevel Touch” technologies.

“DFR”: Dual-Frequency-Response, provide wider bandwidth response and higher energy absorption. It can be decreased the power consumption and improved the touch allocation excursion.

Basic Advantages of SAW:

* Pure-glass touchscreens for superior image clarity, resolution, and light transmission

* Durable, scratch-resistant, and vandal-proof glass surfaces

* Antiglare glass option

* Stable, "drift-free" operation for touch response that's always accurate

* Superior touchscreen response:

Fast—efficient algorithms and electronics

Sensitive—recognizes touch location and pressure

* Finger, gloved hand, and soft stylus activation

* Highest touchpoint density in the industry: 4096 x 4096

* Flat and spherical touchscreen options for design flexibility

* The longest touchscreen warranty available

Specification:

| Technology | Surface Acoustic Wave(SAW) |
| --- | --- |
| Resolution | 4096*4096 |
| Material | Pure glass |
| Deviation of Error | 2mm |
| Light Transmission | 90%～92% |
| Touch Activation Force | Touch force less than 100g(adjust allowed) |
| Endurance | Scratch-free;More than 50,000,000 touches in one location without failure. |
| Surface Hardness | Mohs' hardness rating of 7 |
| MultiPoint Touch | Software discrimination |
| Response Time | Less than 16ms |
| OperatingTemperature | -20°C to +50°C |
| Storage Temperature | -40°C to +70°C |
| Humidity | 10%-90% RH at 40°C, noncondensing |
| Operation Altitude | 3000m |
| Agency Approval | CE, FCC |

Controller: 4001S

Electrical Parameter

Supply Voltage and Current
·+12 Vdc, nominal（+9 Vdc to +15 Vdc）
·100 mA, typical at +12 Vdc. Average power dissipation is 1.2 W, typical.
·Supply must be capable of sourcing 200 mA, minimum.
·Total noise and ripple requirement must be less than 100 mV (p-p) for frequencies below 1 MHz, and less than 50 mV (p-p) for frequencies above 1 MHz.